Calibration User Manual V0.01

Hardware  setting
1,come into image quality,choose “RAW”and “—”
2,manual focus
3，supports cannon 7D and 70D only

1.Initializer

1, calibration mode : Full-screen calibration ,  Manual calibration

2.Online control

A, Local calibration : standalone calibration , need to keep the parameter( COM port, frequency, resolution) same as the setting of sending card .

B,Online calibration: two computers connected to the internet , the first computer connected to the screen , the second computer controlled the first computer to            calibration by internet

3. calibration data :

A, More than one receiving cards need to load the connection file

B,Fill in the resolution( width and the height) of the screen

C,Load the calibration file ( RVS)

D,The default directory would be empty each time before a new calibration ( suggest saving the calibration data to the custom directory)

2.Calibration type : 1, brightness calibration , can set the expected brightness by clicking “next”

2, Colour calibration ,can set  colour conversion of multiple batch cabinets

3.Partition calibration

1, Partition : A,  regular partition , set partition size by clicking”next”

B,

2, Partition calibration

A, Data acquisition : come into the data acquisition interface

B,Save to the hardware : save the data to the receiving card

C,Save to file : save calibration data to a local file (RVS)

A - 1, camera connection: software connect to the camera

A - 2,preview : preview window shows the camera collected pixels

A - 3,zoom: magnify image (under the manual focus mode)

A - 4,measuring: control the camera to calibration by software

A - 5,”last and next” : last zone and next zone

A - 6,save: save calibration data to the receiving card

A - 7,reference dots: the discrepancy light dots between partitions (used to eliminate the differences between partitions)

A - 8,border dots: removal the pixels which blocked by the edges of the screen

A - 9,effect: view the effect after calibration

2,Online control
  A, Local calibration : standalone calibration , need to keep the parameter( COM port, frequency, resolution) same as the setting of sending card .
  B,Online calibration: two computers connected to the internet , the first computer connected to the screen , the second computer controlled the first computer to            calibration by internet 
    Otherwise, online calibration need to work with Ledset.(download link:http//:www.linsn.com)